## Slide 1: ELEC2665 Unit 2
Dr Craig A. Evans

## Slide 2: 2.1 – Assembly Language I
Dr Craig A. Evans

## Slide 3: Outline
Machine language
Assembly language
Hack computer architecture
Hack machine language
Examples
CPU Emulator

## Slide 4: Machine Language

## Slide 5
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 6
Machine language is also known as the instruction set of the processor
Exists on the hardware/software interface
Different ways of looking at it:
  It is a programmer-oriented abstraction of the hardware platform
  ...or you can view the hardware as being the actual implementation of the machine language abstraction
The lowest-level coding possible!
The instructions typically manipulate memory using a processor and a set of registers

## Slide 7: Memory
Memory loosely describes a device that stores data and instructions
At the top-level each data element or instruction (word) is stored at a unique address in the memory
We access a particular word by supplying its address
Notation:
  Memory[address]
  RAM[address]
  M[address]

## Slide 8: Processor
The processor is usually called the central processing unit (CPU)
It is capable of performing a fixed set of elementary operations:
  Arithmetic and logical operations (by the ALU)
  Memory access operations
  Control operations (e.g. branching)
The operands for the operations are usually loaded from registers or selected memory locations
The results of the operations can either be stored in registers or back into selected memory locations

## Slide 9: Registers
Accessing memory is a relatively slow operation – the memory is usually completely separate from the CPU
Therefore CPUs usually have a small collection of registers inside the CPU that can be used to store single values
Act as high-speed local memory
Allows the CPU to process and manipulate data quickly and minimise memory access
e.g. ARM® Cortex®-M microcontrollers have 13 (R0 to R12) 32-bit registers for general-purpose use

## Slide 10: Load/Store Architecture
In a Load/Store architecture, there are two types of instructions
Memory access operations copy words from memory to registers in the CPU and vice versa
ALU operations carry out arithmetic and logical operations on registers and store the result back in registers
i.e. ALU operations can only be carried out on registers and not memory locations
RISC machines (such as ARM) typically have a load/store architecture
Different to register memory architecture (usually CISC – x86)

## Slide 11: Assembly Language

## Slide 12
A machine language program is a series of coded instructions
e.g. An instruction for a 16-bit machine may be 1010 0011 0010 1001
We need to understand the instruction set of the underlying hardware platform in order to know what the instruction does
For example, the instruction above may set the value of register 3 to be the sum of register 2 and register 9

## Slide 13
Writing programs in machine code is not feasible
Therefore symbolic versions of machine code also exists
Mnemonics are used as labels for operations and hardware elements
The symbolic notation is called assembly language
An assembler converts the assembly language to binary
The previous instruction could be written as
ADD R3,R2,R9 // R3 = R2 + R9

## Slide 14
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
.asm
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
0000000000000001
1110001100001000
0000000000010110
1110101010000111
.hack
Assembler

## Slide 15: Hex Editor
The assembler translates each assembly command into a binary machine instruction
These are often called binary files (.bin)
We can use Hex Editors to load and edit the raw binary files
They usually show the hexadecimal equivalent of the binary instruction and ASCII interpretation

## Slide 16: Programmers
The binary files contain the 0’s and 1’s that are loaded into the Read-only Memory (ROM)
In MCU’s the binary instructions are loaded to the Flash memory
This is usually done using an external Flash programmer
MCU’s often have bootloaders that allow us to copy the binary file over serial with a programmer
Programmer

## Slide 17: ROMs

## Slide 19: Hack Computer Architecture

## Slide 20
The Hack computer is a 16-bit machine
Consists of CPU, instruction memory (ROM) and data memory (RAM)
Harvard architecture (different buses for data and instructions)
Both memories are 16-bits wide with 15-bit address space
Two memory-mapped I/O devices:
  Screen
  Keyboard
Two 16-bit registers: A (address and data) and D (data only)

## Slide 21: Simplified Architecture
ALU
Mux
D register
A register
RAM
ROM
PC
Decoder
Notes: Not Load/Store

## Slide 22: Data sources
Two registers in the Hack computer, A and D
The computer can also access data stored in RAM
The RAM address to access is always the current value of the A register
i.e. Memory[A]
or just M for short
Takes two instructions to access M:
  First set A to the required address
  Then read/write from/to M

## Slide 23
ALU
Mux
D
A/M
D register
A register
A
M
RAM
ROM
PC
Decoder

## Slide 24: D-Register Uses
D is purely used to store data values
Can set the value directly to 0, 1 or -1 using ALU operations
D = 1
Cannot be set to other literal values directly
D = 67 is not valid
Values are usually loaded from M or A
D = A

## Slide 25: A-Register Uses
A has three uses:
Facilitate direct access to data memory (RAM) by storing the address M refers to
Store data. The only way to load a literal value into our programs is by loading A with that value
Facilitate direct access to the instruction memory (ROM). When a jump command is executed the instruction stored at the address stored in A is fetched in the next cycle.

## Slide 26: A-Instruction
The A-instruction is used to set the A-register to a 15-bit value
Bit 15 is 0 for an A-instruction
e.g. the following command will load 15 into the A-register
@15
Note the @ syntax and not assignment = e.g. A = 15 is invalid
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v

## Slide 27: C-Instruction
The C-instruction is the workhorse of the Hack computer and handles the computations that are carried out
It is made up of a destination to store the result in (optional), the computation to carry out and any jump condition that is required (optional)
dest = comp;jump
comp;jump
dest = comp

## Slide 28
Bit 15 is 1 for a C-instruction
Bits 14 and 13 are not used
The a-bit is used to select between A and M
The six c-bits are used to select the computation to carry out
The three d-bits are used to set the destination to store the result in (a combination of A, D and M)
The three j-bits specify the jump condition
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 29: Computation
The computation bits determine which operation to carry out
The operation is carried out by the ALU
The 6 c-bits are the same as the 6 instruction bits of the ALU
28 different instructions in the instruction set
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 30
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 31: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register
The result of the computation (ALU output) is fed to one of three locations depending on the d-bits

## Slide 32: Jump
The jump bits tell the CPU what to do next
Typically it will fetch the next instruction in the ROM
If a jump condition has been specified in the C-instruction then the PC will be loaded with a new address if certain conditions are met
The address to jump to is the current value stored in A
This must be loaded into A using the A-instruction before carrying out the C-instruction with a jump specified
Whether the jump occurs or not depends on whether the output of the ALU meets the jump condition

## Slide 33
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 34
ALU
Mux
D
A/M
D register
A register
A
M
RAM
ROM
PC
a
Decoder

## Slide 35: Examples

## Slide 36: Loading values into registers
A and D can both act as data registers and used to hold values
They can easily be set to 0, 1 or -1 using ALU computations
Simply set the destination of the instruction as the relevant register
Use the required computation
D = 1 // set D reg to 1
D = 0 // set D reg to 0
D = -1 // set D reg to -1
A = 1 // set A reg to 1
A = 0 // set A reg to 0
A = -1 // set A reg to -1
dest = comp;jump
comp;jump
dest = comp

## Slide 37
M (RAM) can also be used to store data
Before writing to RAM we must select the address using the A-instruction
We may also wish to copy the contents of the D or A register to a particular RAM location
@5 // set address to 5
M = 1 // RAM[5] = 1
@12 // set address to 12
M = D // RAM[12] = D

## Slide 38: Storing literals in D or A
To load literals values (other than 0, 1 or -1) into registers we must use an A-instruction
The A-instruction allows us to load a 15-bit number into A
Simple to store a literal value in D e.g.
@99 // store 99 in A
D = A // D = 99

## Slide 39: Storing literals in RAM
To store a literal in M takes another A-instruction to set the RAM address e.g.
@57 // store 57 in A
D = A // Use D as a temporary holding area
@10 // store 10 in A, this sets the memory address
M = D // RAM[10] = 57

## Slide 40: CPU Emulator

## Slide 41
We run our assembly code in the CPU Emulator
This tool emulates the behaviour of the Hack computer
Once you have finished building the Hack computer you can run machine code in the Hardware Simulator
Using the CPU Emulator we can load assembly code (.asm) directly
It automatically assembles it into the binary .hack files
These are the raw 0’s and 1’s that are loaded in the ROM
We can also load .hack files we’ve assembled using the supplied Assembler

## Slide 45: Hack Instruction Set Summary

## Slide 46
dest = comp;jump
comp;jump
dest = comp
Dest | Jump | Comp |  |  | 
null | null | 0 | 1 | -1 | D&A
M | JGT | D | A | M | D&M
D | JEQ | !D | !A | !M | D¦A
MD | JGE | -D | -A | -M | D¦M
A | JLT | D+1 | A+1 | M+1 | 
AM | JNE | D-1 | A-1 | M-1 | 
AD | JLE | D+A | D+M | A-D | 
AMD | JMP | D-A | D-M | M-D | 

## Slide 47: 2.2 – Assembly Language II
Dr Craig A. Evans

## Slide 48
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 49: Outline
Symbols
Control statements
  Branching
  Loops
I/O
Hack Instruction Set Summary

## Slide 50: Symbols

## Slide 51
Previously we have seen that data values can be stored in specific RAM locations
We have done this directly using constants
e.g. the following code will store 99 in RAM[3]
@99
D=A
@3
M=D

## Slide 52
Another way to refer to memory locations is by using symbols
There are three ways of using symbols in the Hack assembly programs:
Pre-defined symbols
Label symbols
Variable symbols

## Slide 53: Pre-defined Symbols
Virtual registers
  RAM addresses 0 to 15 can be referred to using the symbols R0 to R15
  This mimics the architecture of typical processors that have a small number of high-speed registers inside the CPU itself
Predefined pointers
  SP, LCL, ARG, THIS, THAT are pre-defined and refer to addresses 0 to 4 respectively
  Can be used together with R0 to R4
  Used in the implementation of the Virtual Machine in Part II
I/O pointers
  SCREEN and KBD refer to 16384 (0x4000) and 24576 (0x6000) and are the base-addresses of the I/O memory maps

## Slide 54
ALU
Control
Unit
Program Counter
Memory Address Register
Instruction Register
Memory Buffer Register
Incrementer
Memory
R4
R5
R6
R3
R2
R7
R1
R0
Register Bank

## Slide 55: Label Symbols
These are user-defined symbols
They label the destination of jump commands
Declared using the syntax
(xxx)
xxx refers to the instruction memory (ROM) location holding the next command to be executed
i.e. value to be loaded into the PC
Can be defined only once in the code

## Slide 56: Variable Symbols
These are user-defined symbols
Any symbol XXX that is not pre-defined or a label is treated as a variable
Automatically assigned a RAM address starting at 16 (0x0010)
e.g. Suppose @sum is the first variable used in the code
It will be stored in RAM[16]
@total is the next variable and will be stored in RAM[17]

## Slide 57: Convention and Syntax
Constants must be non-negative and written in decimal
Symbol names can be any sequence of letters (upper- and lower-case), numbers, underscore, dot, $ and :
  Cannot begin with a digit
Convention:
  Variables are lower-case
  Labels are upper-case
  Commands (mnemonics) are upper-case
White space is ignored
// denotes a comment that is ignored

## Slide 58: Control Statements

## Slide 59
We’ll now look how to implement common code constructs in Hack assembly
High-level C provides two main ways of flow control, branching and loops
Branching is usually decision-based and the program can flow down different branches (typically depending on whether a relational operation is true)
Loops allow a portion of code to be repeated a specified number of times (typically depending on whether a relational operation is true)

## Slide 60: If logic
if (RAM[0] > 100) {
RAM[1] = 5;
}
0 @R0
1 D=M // store R0 in D
2 @100
3 D=D-A // R0 – 100
4 @IF_TRUE // @8
5 D;JGT // if D>0 then R0 > 100
6 @CONT // @12
7 0;JMP
// unconditional jump if false
(IF_TRUE)
8 @5
9 D=A
10 @R1
11 M=D
(CONT)

## Slide 61: If/Else logic
if (RAM[0] > 100) {
RAM[1] = 5;
}
else {
RAM[1] = 7;
}
0 @R0
1 D=M // store R0 in D
2 @100
3 D=D-A // R0 – 100
4 @IF_TRUE // @12
5 D;JGT // if D>0 then R0 > 100
6 @7
7 D=A
8 @R1
9 M=D
10 @CONT // @16
11 0;JMP
(IF_TRUE)
12 @5
13 D=A
14 @R1
15 M=D
(CONT)

## Slide 62: While logic
// Adds 1+2+3+4+5
int i = 1;
int sum = 0;
while (i <= 5){
sum += i;
i++;
}
0 @i // RAM[16]
1 M=1 // i=1
2 @sum // RAM[17]
3 M=0 // sum=0
(LOOP)
4 @i // @16
5 D=M // D = i
6 @5
7 D=D-A // D = i - 5
8 @CONT // @18
9 D;JGT // if(i-5)>0 goto CONT (18)
10 @i // @16
11 D=M // D = i
12 @sum // @17
13 M=D+M // sum += i
14 @i
15 M=M+1 // i++
16 @LOOP // @4
17 0;JMP // goto LOOP (line 4)
(CONT)
18

## Slide 63: While logic
// Adds 1+2+3+4+5
int i = 1;
int sum = 0;
while (i <= 5){
sum += i;
i++;
}
0 @i // RAM[16]
1 M=1 // i=1
2 @sum // RAM[17]
3 M=0 // sum=0
(LOOP)
4 @i // @16
5 D=M // D = i
6 @5
7 D=D-A // D = i - 5
8 @CONT // @18
9 D;JGT // if(i-5)>0 goto CONT (18)
10 @i // @16
11 D=M // D = i
12 @sum // @17
13 M=D+M // sum += i
14 @i
15 M=M+1 // i++
16 @LOOP // @4
17 0;JMP // goto LOOP (line 4)
(CONT)
18

## Slide 64: Conflicting use of the A-register
The A-register can be used to select a data memory (RAM) location for a subsequent C-instruction involving M
@15
M=D
It can also be used to select an instruction memory (ROM) location for a subsequent C-instruction involving a jump
@CONT
D;JGT

## Slide 65
Therefore to avoid conflicting use, you should not use C-instructions with a jump that contain a reference to M
@67
D=M;JGT
This will copy RAM[67] to D-register and then jump to instruction 67 in ROM

## Slide 66: I/O

## Slide 67
The keyboard and screen are memory-mapped peripherals
Means the memory associated with them appears to be a part of the main memory
Each has a particular address (or range of addresses) associated with them
Common in microcontrollers – Flash, RAM and peripherals all appear to be in the same memory space despite being physically separate devices

## Slide 68: Keyboard
Keyboard (KBD) is essentially a 16-bit register at memory location 24576 (0x6000)
When read it contains the 16-bit ASCII value of the current key being pressed (0 when no key is pressed)
  ‘0’ to ‘9’ (48 to 57)
  ‘A’ to ‘Z’ (65 to 90)
  ‘a’ to ‘z’ (97 to 122)

## Slide 69
Key Pressed | Code | Key Pressed | Code
newline | 128 | end | 135
backspace | 129 | page up | 136
left arrow | 130 | page down | 137
up arrow | 131 | insert | 138
right arrow | 132 | delete | 139
down arrow | 133 | esc | 140
home | 134 | F1 - F12 | 141 - 152

## Slide 70: Screen
The ‘screen’ has a resolution of 256 rows by 512 columns
Represented by a 8K memory map starting at 16384 (0x4000)
Each row is represented by 512/16 = 32 words (16-bit each)
Each bit represents a pixel (1 = black , 0 = white)
Pixel on row r and column c is the c%16 bit in the word at RAM[16834+32r+c/16]
Tip: -1 in binary is 1111 1111 1111 1111

## Slide 71: Hack Instruction Set Summary

## Slide 72
dest = comp;jump
comp;jump
dest = comp
Dest | Jump | Comp |  |  | 
null | null | 0 | 1 | -1 | D&A
M | JGT | D | A | M | D&M
D | JEQ | !D | !A | !M | D¦A
MD | JGE | -D | -A | -M | D¦M
A | JLT | D+1 | A+1 | M+1 | 
AM | JNE | D-1 | A-1 | M-1 | 
AD | JLE | D+A | D+M | A-D | 
AMD | JMP | D-A | D-M | M-D | 

## Slide 73: Symbols
Symbol | Value
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4

## Slide 74: 2.3 – Computer Architecture
Dr Craig A. Evans

## Slide 75
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 76: Outline
Stored-program Computer
Hack Computer
Memory
CPU
Computer

## Slide 77: Stored Program Computer

## Slide 78
A computer is a fairly unique machine in that it consists of a fixed hardware platform yet it can carry out an almost infinite number of tasks
It does this by running different software – games, web browsers, media players, word processors, custom embedded firmware etc.
The software consists of instructions that are stored within the computer memory and can be changed by loading new instructions into the memory
This is called the stored-program concept
The computer then fetches these instructions from memory and executes them

## Slide 79: Components
Processor
Data
Instructions
Address
Data
Processor – the thing that actually executes the instructions
Memory - stores the instructions themselves and any data required
Buses – used to move the data and instructions back and forth between the processor and memory

## Slide 80: Fetch-Execute Cycle
In essence a computer simply executes a series of instructions
Executing an instruction involves the following steps:
  The ALU computing some operation
  Writing the result to a register and/or memory location
  Deduce which instruction to execute next

## Slide 81: Architecture
The term be used in different ways:
The instruction set architecture (ISA) describes the instructions that the computer can execute and is the view that is most important to a computer programmer
The term microarchitecture refers to the way in which the ISA is implemented in hardware i.e. an ADD instruction may be implemented using a binary adder
The computer architecture describes the complete system including the processor, memory, buses and peripherals

## Slide 82: Hack Computer

## Slide 83
At this point in the course we have built the entire Hack chipset:
  Nand, Not, And, Or, Xor, Mux, Dmux, Not16, And16, Or16, Mux16, Or8Way, Mux4Way16, Mux8Way16, DMux4Way, DMux8Way
  HalfAdder, FullAdder, Add16, Inc16, ALU
  DFF, Bit, Register, RAM8, RAM64, RAM512, RAM4K, RAM16K, PC
This project is the culmination of the hardware design and implements the final few pieces of the Hack computer:
  Memory, CPU, Computer

## Slide 84: Specification
16-bit machine
Physically separate instruction and data memory
  32K instruction memory (ROM)
  16K data memory (RAM)
512 x 256 screen (black and white)
Standard keyboard
Executes programs written in the Hack machine language

## Slide 85: Memory

## Slide 86: Instruction memory
The ROM is pre-loaded with a program written in the Hack machine language
Consists of 32K 16-bit registers
Each register can contain an instruction
out = ROM32K[address]
Built-in – do not need to implement
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 87
We won’t worry about how the program is loaded to the ROM
We’ll just use the simulation tools to load in a assembled .hack file
In reality a programmer is used to write the binary instructions to the Flash memory (for a microcontroller)
For an actual ROM device, the binary image is burned in the factory and cannot be changed
Some microcontrollers have electrically-erasable programmable read-only memory (EEPROM)
Typically just a few kilobytes

## Slide 88: Data memory
To read from memory (RAM[k]) we set the address to k and then probe out
To write to memory (RAM[k] = x) we set the address to k, set in to x, set load to 1 and then clock it in
We’ve already built this
load
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 89: Screen
Has basic RAM chip functionality (8K)
Base address 0x4000
The bit contents of the screen chip is known as the screen memory map
Built-in, we don’t have to implement
Essentially just RAM but with a GUI element in the CPU Emulator
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 90
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 91: Keyboard
16-bit register that contains the ASCII code of the key currently being pressed
Base address 0x6000
Built-in, we don’t have to implement
Essentially just a read-only 16-bit register with a GUI element in the CPU Emulator
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 92: Memory Map
The RAM, Screen and Keyboard appear together in the same memory map
To the programmer they appear as a single memory device
Each has a different address range
Data
Screen memory map
Keyboard map
Memory
Keyboard
Screen
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 93: Physical Implementation
The Memory.hdl chip is essentially a package that integrates the RAM, Screen and Keyboard into a single contiguous address space
RAM - 0 to 16383 (0x0000 to 0x3FFF)
Screen – 16384 to 24575 (0x4000 to 0x5FFF)
Keyboard – 24576 (0x6000)
load
out
in
16
15
16
RAM16K
(16K mem. chip)
address
0
16383
Screen
(8K mem. chip)
16384
24575
24576
Keyboard
(one register)
Memory
Keyboard
Screen
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 94: CPU

## Slide 95: Simplified Architecture
ALU
Mux
D register
A register
RAM
ROM
PC
Decoder
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org
Notes: Not Load/Store

## Slide 96
Internally the CPU is composed of the ALU, A-register, D-register and PC along with various combinational chips
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 97: Execute Logic
If comp contains M then it is read from inM
If dest contains M then the ALU output is piped to outM, the address (A-register) appears on addressM and writeM is asserted
dest = comp;jump
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 98: Fetch Logic
The instruction may contain a jump directive as signified by the jump bits in the instruction
If reset is 0 and the ALU flags indicate a jump should occur then the value of A is loaded into the PC. Otherwise the value in PC is incremented
If reset is 1 then the value in PC is set to 0.
dest = comp;jump
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 99: C-instruction
Bit 15 is 1 for a C-instruction
Bits 14 and 13 are not used
The a-bit is used to select between A and M
The six c-bits are used to select the computation to carry out
The three d-bits are used to set the destination to store the result in (a combination of A, D and M)
The three j-bits specify the jump condition
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 100: CPU Implementation
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 101
© indicates a control bit
The decode part is not a chip part, but represents that the control bits be decoded from the instruction somehow

## Slide 102: Computer

## Slide 103: Interface
The Computer is the top-most chip in the Hack platform
The pinnacle of your journey from NAND gates to a ‘real’ computer
ELEC2655 Gates to PC
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 104: Implementation

## Slide 105: API

## Slide 106
Chip Name: | Memory
Inputs: | in[16], load, address[15]
Outputs: | out[16]
Function: | The complete address space of the Hack computer's memory, including RAM and memory-mapped I/O. The chip facilitates read and write operations, as follows: Read: out(t) = Memory[address(t)](t) Write: if load(t-1) then Memory[address(t-1)](t) = in(t-1) In words: the chip always outputs the value stored at the memory location specified by address. If load==1, the in value is loaded into the memory location specified by address. This value becomes available through the out output from the next time step onward. Address space rules: Only the upper 16K+8K+1 words of the Memory chip are used. Access to address>0x6000 is invalid. Access to any address in the range 0x4000-0x5FFF results in accessing the screen memory map. Access to address 0x6000 results in accessing the keyboard memory map. The behavior in these addresses is described in the Screen and Keyboard chip specifications given in the book.
Comment: | 
Chip Name: | CPU
Inputs: | inM[16], instruction[16], reset
Outputs: | outM[16], writeM, addressM[16], pc[15]
Function: | The Hack CPU, consisting of an ALU, two registers named A and D, and a program counter named PC. The CPU is designed to fetch and execute instructions written in the Hack machine language. In particular, functions as follows: Executes the inputted instruction according to the Hack machine language specification. The D and A in the language specification refer to CPU-resident registers, while M refers to the external memory location addressed by A, i.e. to Memory[A]. The inM input holds the value of this location. If the current instruction needs to write a value to M, the value is placed in outM, the address of the target location is placed in the addressM output, and the writeM control bit is asserted. (When writeM==0, any value may appear in outM). The outM and writeM outputs are combinational: they are affected instantaneously by the execution of the current instruction. The addressM and pc outputs are clocked: although they are affected by the execution of the current instruction, they commit to their new values only in the next time step. If reset==1 then the CPU jumps to address 0 (i.e. pc is set to 0 in next time step) rather than to the address resulting from executing the current instruction.
Comment: | 

## Slide 107
Chip Name: | Computer
Inputs: | reset
Outputs: | 
Function: | The HACK computer, including CPU, ROM and RAM. When reset is 0, the program stored in the computer's ROM executes. When reset is 1, the execution of the program restarts. Thus, to start a program's execution, reset must be pushed "up" (1) and "down" (0). From this point onward the user is at the mercy of the software. In particular, depending on the program's code, the screen may show some output and the user may be able to interact with the computer via the keyboard.
Comment: | 

## Slide 108: Verified?
Memory | ☐ | CPU | ☐ | Computer | ☐

## Slide 109: 2.4 – Assembler
Dr Craig A. Evans

## Slide 110
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 111: Outline
Machine Language (recap)
Instruction Format
Symbols
Assembly Procedure
Example

## Slide 112: Machine Language

## Slide 113
A machine language program is a series of coded instructions
e.g. An instruction for a 16-bit machine may be 1010 0011 0010 1001
We need to understand the instruction set of the underlying hardware platform in order to know what the instruction does
For example, the instruction above may set the value of register 3 to be the sum of register 2 and register 9

## Slide 114
Writing programs in machine code is not feasible
Therefore symbolic versions of machine code also exists
Mnemonics are used as labels for operations and hardware elements
The symbolic notation is called assembly language
An assembler converts the assembly language to binary
The previous instruction could be written as
ADD R3,R2,R9 // R3 = R2 + R9

## Slide 115
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
.asm
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
0000000000000001
1110001100001000
0000000000010110
1110101010000111
.hack
Assembler

## Slide 116: Instruction Format

## Slide 117: A-Instruction
The A-instruction is used to set the A-register to a 15-bit value
Bit 15 is 0 for an A-instruction
e.g. the following command will load 15 into the A-register
@15
Note the @ syntax and not assignment = e.g. A = 15 is invalid
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v

## Slide 118: C-Instruction
The C-instruction is the workhorse of the Hack computer and handles the computations that are carried out
It is made up of a destination to store the result in (optional), the computation to carry out and any jump condition that is required (optional)
dest = comp;jump
comp;jump
dest = comp

## Slide 119: C-instruction
Bit 15 is 1 for a C-instruction
Bits 14 and 13 are not used
The a-bit is used to select between A and M
The six c-bits are used to select the computation to carry out
The three d-bits are used to set the destination to store the result in (a combination of A, D and M)
The three j-bits specify the jump condition
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 120: Computation
The computation bits determine which operation to carry out
The operation is carried out by the ALU
The 6 c-bits are the same are the 6 instruction bits of the ALU
28 different instructions in the instruction set
Elements of Computing Systems, Nisan & Schocken, MIT Press, www.nand2tetris.org

## Slide 121: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 122: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register
The result of the computation (ALU output) is fed to one of three locations depending on the d-bits

## Slide 123: Jump
The jump bits tell the CPU what to do next
Typically it will fetch the next instruction in the ROM
If a jump condition has been specified in the C-instruction then the PC will be loaded with a new address if certain conditions are met
The address to jump to is the current value stored in A
This must be loaded into A using the A-instruction before carrying out the C-instruction with a jump specified
Whether the jump occurs or not depends on whether the output of the ALU meets the jump condition

## Slide 124: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 125: Symbols

## Slide 126
Without symbols the assembly process is trivial
It is simply decoding the A- and C-instructions according to the Hack machine language specification
When the assembly code has symbols the process becomes slightly more difficult and requires two passes through the code
A look-up table is created that contains all the pre-defined symbols and their numeric values

## Slide 127: Pre-defined Symbols
Symbol | Value
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4

## Slide 128: User-defined Symbols
User-defined labels (XXX) are added to the look-up table on the first-pass of the code
User-defined symbols @xxx are added on the second pass and are automatically allocated an address in RAM (starting at 16)

## Slide 129: Assembly Procedure

## Slide 130
Initialisation
  Create a look-up table and populate it with the pre-defined symbols
  Strip out comments and white-space
First-pass
  Go through the source code line-by-line (without generating code)
  For each label declaration (LABEL) that appears add the pair <LABEL,n> to the look-up table
Second-pass
  Go through the source code line-by-line
  Translate C- and A-instructions with literals to binary instructions
  If the line is a @symbol then look in the look-up table
    If it is found, replace with numeric value and then translate to binary as normal
    If not found, it must be a variable, so add to look-up table at the next available RAM address and translate to binary
    RAM addresses for variables start at 16

## Slide 131: Example (no symbols)

## Slide 132
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3
0 | @0
1 | D=M
2 | @1
3 | D=D+M
4 | @9
5 | D=D+A
6 | @2
7 | M=D
8 | 
9 | 
10 | 
11 | 

## Slide 133: Example (with symbols)

## Slide 134: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 135
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3
0 | @i
1 | M=1
2 | @sum
3 | M=0
(LOOP) | 
4 | @i
5 | D=M
6 | @5
7 | D=D-A
8 | @CONT
9 | D;JGT
10 | @i

## Slide 136
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3
11 | D=M
12 | @sum
13 | M=D+M
14 | @i
15 | M=M+1
16 | @LOOP
17 | 0;JMP
(CONT) | 
18 | 
19 | 
20 | 
21 | 

## Slide 137: First-pass
Go through code and look for (LABELS)
Add the <LABEL,n> pair to the look-up table
n is the next instruction (line) number

## Slide 138: Second-pass
Go through line-by-line
Translate C- and A-instructions with literals to binary instructions
If a line is a @symbol then look in look-up table
Replace with numeric value if found
If not found then add to next RAM slot (starting at 16)
Replace with numeric value
Translate to binary instruction

## Slide 139: Testing
The assembled code should be typed into a text file with .hack extension
Can then be loaded into the CPU Emulator
Can also use the supplied Assembler tool to assemble the .asm source file and compare to your manually assembled .hack file
  Load the .asm source file (File/Load Source File)
  Load your manually assembled .hack file (File/Load Comparison File)
  Step through the assembly procedure and it will compare the files line by line

## Slide 140: Assembly Tables

## Slide 141: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 142: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register

## Slide 143: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 144: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 145
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 146
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 147
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 148
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 149: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 150: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register

## Slide 151: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 152: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 153
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 154
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 155
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 156
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 157: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 158: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register

## Slide 159: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 160: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 161
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 162
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 163
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 164
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 165: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 166: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register

## Slide 167: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 168: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 169
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 170
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 171
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 172
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 173: Comp
zx | nx | zy | ny | f | no | comp mnemonic |  | alu
c1 | c2 | c3 | c4 | c5 | c6 | a=0 | a=1 | 
1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1
1 | 1 | 1 | 0 | 1 | 0 | -1 |  | -1
0 | 0 | 1 | 1 | 0 | 0 | D |  | x
1 | 1 | 0 | 0 | 0 | 0 | A | M | y
0 | 0 | 1 | 1 | 0 | 1 | !D |  | !x
1 | 1 | 0 | 0 | 0 | 1 | !A | !M | !y
0 | 0 | 1 | 1 | 1 | 1 | -D |  | -x
1 | 1 | 0 | 0 | 1 | 1 | -A | -M | -y
0 | 1 | 1 | 1 | 1 | 1 | D+1 |  | x+1
1 | 1 | 0 | 1 | 1 | 1 | A+1 | M+1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | D-1 |  | x-1
1 | 1 | 0 | 0 | 1 | 0 | A-1 | M-1 | y-1
0 | 0 | 0 | 0 | 1 | 0 | D+A | D+M | x+y
0 | 1 | 0 | 0 | 1 | 1 | D-A | D-M | x-y
0 | 0 | 0 | 1 | 1 | 1 | A-D | M-D | y-x
0 | 0 | 0 | 0 | 0 | 0 | D&A | D&M | x&y
0 | 1 | 0 | 1 | 0 | 1 | D¦A | D¦M | x¦y

## Slide 174: Destination
d1 | d2 | d3 | Mnemonic | Destination
0 | 0 | 0 | null | Not stored anywhere
0 | 0 | 1 | M | Memory[A]
0 | 1 | 0 | D | D register
0 | 1 | 1 | MD | Memory[A] and D
1 | 0 | 0 | A | A register
1 | 0 | 1 | AM | A register and Memory[A]
1 | 1 | 0 | AD | A register and D register
1 | 1 | 1 | AMD | A register, Memory[A] and D register

## Slide 175: Jump
j1 | j2 | j3 | Mnemonic | Destination
out < 0 | out = 0 | out > 0 |  | 
0 | 0 | 0 | null | No jump
0 | 0 | 1 | JGT | If out > 0 then jump
0 | 1 | 0 | JEQ | If out = 0 then jump
0 | 1 | 1 | JGE | If out ≥ 0 then jump
1 | 0 | 0 | JLT | If out < 0 then jump
1 | 0 | 1 | JNE | If out ≠ 0 then jump
1 | 1 | 0 | JLE | If out ≤ 0 then jump
1 | 1 | 1 | JMP | Jump

## Slide 176: Lookup Table
Pre-defined Symbol | Number
SCREEN | 16384
KBD | 24576
R0 to R15 | 0 to 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
User-defined Symbol | Number

## Slide 177
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 178
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 179
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3

## Slide 180
32768 | 16384 | 8192 | 4096 | 2048 | 1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | v | v | v | v | v | v | v | v | v | v | v | v | v | v | v
1 | 1 | 1 | a | c1 | c2 | c3 | c4 | c5 | c6 | d1 | d2 | d3 | j1 | j2 | j3